Team Calvin & Dr. Schafer

Meeting Minutes II

Date		: January 30, 2007

Time		: 1 – 1.30 pm

Location	: Engineering Learning Center

Items Discussed:

- The synchronous clock on SPI/I2C is faster and easier to use because of chip select to read or write to

- Maxstream uses RS232 wirelessly

- MOSFET driver provides voltage to slam the gate on/off

- Separate control for MOSFETs from the actual MOSFETs

- MOSFET is effectively a capacitor, larger current for greater speed

  - logical one or logical zero (invert/non-invert)

- We could put the lift fan on a power transistor by itself

  - Get a 5A power transistor just in case

- Pulse-Width Modulated signals (from the microcontroller) control the speed, followed by a logical sequence telling whether we are going forward or backwards

  - Logical function turns correct pairs on

  - Can achieve dynamic breaking by turning two on

  - Then use a drive section with MOSFETs, protected by diodes, to switch the power

Action Items:

- View SPI pdf document and attempt to use SourceBoost to talk to chipcon

  - Chipcon pins:  Vreg enable, reset, the right side (these are the signals that come off from the daughter card to the microcontroller)

  - Figure out how the microcontroller is connected to the chipcon (specified in the pdf document)

  - Can we have two independent PWM signals from the microcontroller?

- Look at H-bridge drivers

  - You can buy an H-bridge that has everything on a chip

  - Get DIP packages for prototyping

- Prepare video demonstration for CRANE reps

- Continue building new hovercrafts