Team Calvin & Dr. Schafer

Meeting Minutes III

Date		: February 6, 2007

Time		: 1 – 1.30 pm

Location	: Engineering Learning Center

Items Discussed:

- The compiling error in the code for the microcontroller may be able to be fixed by canceling the use of interrupts.

- Regarding the SPI communications, the reset must be set to high, the voltage regulator must be enabled, and we must send the command strobe.

- 8 bits are transferred back and forth between the Chipcon and microcontoller

- The master shifts data out of the buffer, the slave shifts data in from the buffer

- Most of the materials needed for the construction of more hovercrafts have been purchased and fitted, however motor propellers and another skirt are still needed

- The sample H-bridge from Allegro has been received, but we must use our own design for the H-bridge that we will use

- We will need a schematic of everything for our final report

Action Items:

- Continue H-bridge research and development

  - Need to develop own design for the H-bridge, but may order them online to see how they work

- Modify code for multi-beacon navigation

- Continue building new hovercrafts

  - Need to purchase certain materials for completion of two more hovercrafts, including a heavy duty trash bag for the skirt, motors, and propellers

- Continued research and testing with Chipcon and the SPI interface

  - Write a function that sends a character and receives a character