Team Calvin & Dr. Schafer

Meeting Minutes VI

Date		: February 27, 2007

Time		: 1 – 1.30 pm

Location	: Engineering Learning Center

Items Discussed:

Matt: working on building the board

- Action: try using Eagle software - download

Mario: working on SPI

- can use the packet sniffer for debugging

- Action:  Chubbs, program a mote to send a packet every few seconds at a medium strength, but it doesn’t really matter at this point

Clem: start to write code for the h-bridge, sending a PWM signal

- should be short code if you don’t care about the last two bits

- set up registers

- set tris bits

- start a timer

- same period, different duty cycles

- C3, C4, C5 used for SPI (tris)

Jeff: performed demo in the Stepan center

- drop diode across the motor, turn off quicker

- put control circuit on the lift fan

- HC works better at slower speeds

- Order propellers for the third HC

*Other groups have issues with packaging – we might have issues with this in the future

Miscellaneous Notes:

Look at the format of a zigbee packet – what do they look like

Put char string in an array and then parse it

Two bytes control info, address, payload

Write a fcn that will send back stuff in a structure

Header info in payload

Or fcn that gets an entire frame in an array and then program goes through the array

Least important info is the payload – not used very much

Demonstration Objectives:

- show microcontroller can receive RSSI

- show microcontroller can communicate with H-bridge

- show control of H-bridge works with the motors

- control speed of the fans, doesn’t have to lift the HC

- show send/receive zigbee packets and address of sender