Minutes

Date:			Wednesday, February 14, 2007

In Attendance: 	Dr. Schafer, Michael Cozzolino, Colleen O’Hagan, Elizabeth Reed, Andrew Williams

Note:  This was our fourth weekly status meeting.

Additions to product list:

  - No new parts received

Summary of Progress:

- Ultrasonic Sensors

  - It appears that we will be unable to procure samples of the nebulizing transducers due to lack of response from the company.

  - No progress on getting bare transducers.

  - Signal handling provided some odd results with use of a diode rectifying circuit (full and half wave) that may be attributed to insufficient voltage to overcome the voltage drop across the diodes.

- Vibrating Motors

  - Decided to use coin vibrating motors for simplicity and vibration strength

- Infrared

  - We found an error in our circuit setup (missing ground connection) and the new test results show impressive repeatability and accuracy out of water.

  - We are in the process of working out testing time at Rolfs Aquatic Center to perform in-water characterization tests.

  - We are also awaiting the arrival of new environmental covers as well as focusing lenses for testing at a later date.

- RF

  - Attempted to setup RF transmitters again but little progress due to some confusion over operational specs.

  - Using information from Dr. Schafer we will try getting the RF transmitters communicating using the correct input signal.

  - Once we have the RF system working, we will use the output to activate the vibrating motor.

Action items:

- Open items

  - Contact Rolfs Aquatic Center for testing and measurements: Beth

  - Test RF sensors with improved antenna design and correct input signal: Colleen, Mike

  - Characterize the IR sensors in-water: Beth, Drew

  - Order just transducers for ultrasonic signaling: Drew

  - Get ultrasonic/RF signal to actuate vibrator: Colleen, Mike

  - Get another board for parallel testing: Drew

- New Items

  - Contact Mr. Strebinger for designing waterproof pool casing: Beth, Drew

  - Obtain power sources for use at swimming pool (9-volt battery pack from Dr. Schafer, 5-volt pack from Clint Manning): Drew