Minutes

Date:			Wednesday, March 28, 2007

In Attendance: 	Dr. Schafer, Michael Cozzolino, Colleen O’Hagan, Elizabeth Reed, Andrew Williams

Additions to product list:

  - Received two sets of new transmitter/receiver pairs

Summary of Progress:

  - PIR

    - Tested the new PIR sensors in lab and were able to detect a person with much higher sensitivity than the other sensors.

    - Obtained the USBee oscilloscope probe from Dr. Schafer, tested the PIRs using the oscilloscope on a laptop

    - Brought the PIRs to the pool to see their effectiveness in water

    - Were able to detect a person swimming through water

      - Maximum and minimum voltages reached were not constant, but the signal oscillated rapidly when a swimmer swam by

      - With no swimmer, the PIR voltage varied between 2.5 and 2.7V with no rapid changes

    - Need to get hard data readings in order to develop an algorithm

      - Use EEPROM from Dr. Schafer

      - Use A/D converter on microcontroller

    - Need to build a test rig, preferably from the end of the pool using PVC pipe.

    - Need to Develop a board that will fit into the PVC pipe

  - Transmitter/Receivers

    - Had to solder the LC transmitter/receiver pair to a board to test, but could not solder at the specified temperature.  Increased the temperature to accomplish the task

    - Tested the LC transmitter receiver pair on the same board and across the room using an antenna

      - Were able to send a signal and turn on the motor

      - With no signal, motor is off

    - Need to get new batteries with a higher current rating to run the transmitter/receiver pair.

      - Must consider the electrical and mechanical requirements (must be low profile batteries)

    - Need to design a board for the receiver.

Action items:

- Open items

  - Setup the A/D converter on the microcontroller

  - Setup the EEPROM to gather data

  - Characterize PIR sensors in water

  - Develop an algorithm for detecting a swimmer in water

  - Test the developed algorithm

  - Design a board for the PIR

  - Test the new transmitter and receivers

  - Obtain new batteries with a higher current rating

  - Test the transmitter receiver pair inside of a cap and in water

  - Design a board for the transmitter and receiver