Minutes 1/20/09

- List of Subsystems to be presented at Design Review 1

- Temperature sensor is from Microchip- $7.50 processing fee

  - Dave to cont. contact with Microchip Re: temp. sensor

  - Dave already can get 10 samples of PIC18, didn’t get fee

- PIR sensor

  - Received

  - Only has a power, ground, and signal

- Zigbee Daughter Card

  - Believe we have SPI initialized, but don’t know about comm. timing

  - Apparently there is an SPI flag (SSPxIF) that asserts whenever the byte is done being shifted out

  - So in the case of the read, we need to assert the chip select, load the read instruction into the buffer register.  Wait for the SSPxIF flag, then send a junk byte to the Zigbee Card, wait for SPIxIF, and read the byte from the buffer register.

  - Initializing the SPI, match the clocking waveforms between the daughter card and the microcontroller.  CKP=0,CKE=1.

  - Use the USBee logic analyzer on the SPI pins

  - Next step, be able to right to transmit and receive buffers on Zigbee.  Then be able to deal with the state machine of the transceiver.  Then dealing with interrupts.

  - Angela got the Zigbee Mote working properly.  Will have instructions ready soon.

- Board batteries

  - 3.3V all around for the board

  - 9V NiMH batteries

- Next Meeting: 10:00AM Tuesday, January 27th

  - Manager: Riley Fenlon

  - Minutes: Katie Pierret