Minutes 2/17/2009

1.    Subsystems Review

  a) Wireless Communication

- Transmitted a custom data packet

- Need power and LCD for a second Zigbee board

- Will test the range of Zigbee signal

b) Temp Sensor

- Ordered a new 8-pin sensor—is on its way

- Design Review: should demonstrate SPI is working

c) PIR Sensor

- Consider that the lights in LC put out a lot of infrared

- Will decide in future whether to place sensor directly overhead or by a doorway (where it could keep track of number of occupants in room)

- Cannot detect very small movements like a head nod

d) Batteries

- Samples of battery holders ordered

- Design Review: circuitry should be breadboarded

- Schafer will provide batteries

- Test charging capabilities by recharging the batteries used for Zigbee range testing

e) LEDs

- Try breadboarding using a mosfet to increase brightness

f) RTC

- Place a button battery holder on the board as a backup voltage supply

- Keystone has battery holders

g) Packaging

- Many boxes have holes for mounting circuit, but need exact board size before we can choose an appropriate box

2.    Other notes

a) Schematic/board layout

- Will place temp sensor on board but also leave pins for it on the wiring harness

- Board is currently 4” by 5”

- Will meet to double/triple check board

b) Design Review

- Will take place next week in the electronics lab, usual meeting time

- Have hex files for each subsystem saved for quick reprogramming

c) Jumpers

- Natalie has wires and shrink wrap to make more jumpers

- Schafer has header pins