University of Notre Dame

Electrical Engineering Senior Design

The Dream Team

Weekly Meeting: 4PM, Friday January 25th, Engineering Learning Center

Expected Attendance: Andrew Carter (Meeting Leader), Matthew Elliott (Meeting Minutes), Andrew Harms, Benjamin Keller, Dr. Schafer

Meeting Minutes

Start - 4PM

End - 5PM

- Overview of Meeting Goals

- Overall Plan for the Semester

  - Examined our schedule as of now - Microsoft Project: Gantt Chart

  - Each group member defines goals for semester

    - Andrew Carter

      - PCB Layout and Design

      - Microcontroller Integration

      - LCD / Human Interface

    - Matthew Elliott

      - Power / Charging

      - LCD / Human Interface

    - Andrew Harms

      - Zigbee Communication

    - Benjamin Keller

      - USB Communication

  - Goals for Design Review I (February 29)

    - Andrew Carter

      - After finishing PCB layout, use microcontroller to control LCD and keypad. To have a functioning subsystem, the LCD should display arbitrary text, graphics, etc. The keypad is functioning when the microcontroller can interpret key presses. To have a functional subsystem, the LCD must provide the end-user with pertinent data, such as a question or system status. The keypad is functional when the user can input his answer.

    - Matthew Elliott

      - Charge a Li-Poly battery to power the response unit. To have a functioning subsystem, the IC charges a Li-Poly battery. To have a functional system, the IC charges a battery and provides power to the rest of the response unit.

    - Andrew Harms

      - Provide a wireless communication link between the nodes held by students in the classroom and the base station under control of the teacher. To have a functioning subsystem, the Zigbee radio must be able to send and receive packets of data. To have a functional subsystem for our system, two Zigbee radios must be able to establish a communication link and send and receive packets to and from each other.

    - Benjamin Keller

      - Use USB communication to send and receive data to a computer. To have a functioning subsystem, the USB IC must follow standard USB protocol communications with a PC. To have a functional system, the USB IC transmits and receives data necessary to collect student response answers. It also serves as a way of charging the battery.

- Current Status Reports

  - Andy Carter

    - Has ideas for handheld unit casing.

    - Will program microcontroller in C (AVR) using JTAG programmer.

    - Need to find inexpensive keypad mentioned in meeting from California.

    - LCD is causing budget problems.

    - USB board

      - Design is virtually finished.

    - Main board

      - After testing will function as base station since it will be large.

        - There is a lot of wasted space.

        - Final size doesn’t matter on test/base station board.

      - Microcontroller

        - Zigbee built in.

        - 64 pin version

      - Ziff socket

        - Be careful as far as how it is supposed to fold. Look at sample Dr. Schafer has built

        - Will fold backwards.

        - Consider how it may mount, need backlight, hit keypad.

      - Programming jumpers for LCD

      - Keypad header – position may be altered in future.

      - Battery is by far largest thing on board.

      - Power filtering – for testing

      - Battery chip – positioning is tough

        - Solder lug for cooling

        - Try thru DFM

        - DRC freaked out

        - Ask Dr. Schafer about air wires.

        - LED breakout

        - USB must be close to power and battery

      - USB chip

        - Went with crystal not ceramic resonator.

        - MRATA has ceramic resonator for USB.

      - Cheap push button ripoff from Dr. Schafer.

        - Top and bottom ground planes?

          - Problems with power and gnd plane? – two gnd planes = capacitor?

      - Use better diodes

        - Smaller and lower voltage parts can be used

      - Can use 0 ohm resistors on final board

      - Switch T0220 parts to surface mount.

      - Zigbee breakout.

  - Matthew Elliott

    - Battery Charger Unit

      - Currently waiting for board to be made.

      - Battery charger chip and surrounding circuitry will reside on main microcontroller board.

      - Thermistor for battery included on main board.

  - Andrew Harms

    - Working on Zigbee wireless communication.

    - Can use development kit to accomplish goals for Design Review I.

  - Benjamin Keller

    - Currently waiting for USB board to be made.

    - USB board self-contained.

- General Comments

  - All parts still needed are orderable.

  - Main board

    - For handheld

      - use smaller connections, don’t use minis, board house went to micro

      - can make vias smaller - .5 mm spec in Net classes

  - Keypad

    - 10.1 inch spacing

    - 3x4 matrix

    - 7 pins

    - Need pullup resistors on pins so don’t fry microcontroller ( 10k/1k ohm for reading and 200/100 ohm for writing)

    - These may be included in microcontroller.

    - If two keys are pressed, can have 1 output high and 1 output low connected together.

    - Interrupt pins

  - Resonator

    - Subtle differences in part numbers (Mirata)

    - 10 and 20 Mhz frequency

    - Difference in parts – general purpose or not, be careful when ordering – pinouts

  - Think about soldering the QFN

    - may be difficult

    - if using oven, make sure its not on reflow and turned up to 200 C

  - Think about physical layout – keypad/LCD – perhaps have something to catch LCD when it folds

  - Get rid of pwr plane until routing pwr, put decoupling on flip side.

  - Unused pins- bring ou to edge of board for on/off button, reset

  - Handheld

    - Plug in and register

    - When d/ling code

    - Serial EPROM – hardcoced ID

  - Zigbee addresses – you must program yourself.

  - SPI interface

    - USB and Zigbee are on same bus (chip select) because buffered

    - Make sure it runs fast enough

  - When will be confident about main board?

    - Monday

    - Using 0603 surface mount components

    - Dr. Schafer has good 0805 green/red LEDs and 300 ohm resistors

  - Should handroute near microcontroller

    - Use gid

    - Know spacing on ATMEL (.5 mm?)

  - Board house can only go so small – 3 or 1.5 mm , consider what is necessary for QFN

  - Think about starting system up

    - Wait for pwr to stabilize, then reset sys?

  - Andrew Harms needs to leave but ok because we are bullshitting now. Andy talking way too much.

  - Battery

    - Lith poly

  - Talk to Dr. Schafer about board on Tuesday

  - Will use HID for USB

    - Start investingating drivers more

    - Use keyboard or joystick?

    - Dataformatting?

  - Ben should read USB Bible

  - Andy should get board down to 3x5, limit wasted space

    - Add test points – large vias

    - Add jumper, where you want to measure current

  - QFN – can we use pick and place?