Minutes 1/13/2009

1.    List of Subsystems to be presented at Design Review I

  a)PIC18F4455

- Can try to get for free from Microchip through University Program

  - May need to switch micro to match other groups in order for free part

  - Dave will contact

- Look into parts specified for different temperatures

b) PIR sensor

- Ordered but not here yet

- Possibly has a bunch of unnecessary electronics

- Look into a bare bones sensor (cheaper)

c) Power

- 9V nickel metal hydride rechargeable battery is a possible option

- Keystone makes battery connectors (website link on wiki)

e) Directional Indicators

- Super Bright LEDs have arrived

f) ZigBee

- Can get a pair of transmitters

- Jumpers or DC to DC converter may cause the LCD issues

- Angela will help program motes in TinyOS for ZigBee testing

- 11 is lowest channel, goes up through 26

- Packet sniffer plugs into a serial port and detects packets

  - Does not keep up with high data rates

- Critical path delay needs to be considered

2.   Packaging

- Wiki has a link to a website with various packaging

- Need to consider height of components (LEDs, ZigBee), as well as screw placement, etc

3.  Parts

- Dr. Schafer has "in house" parts like standard resistors, caps, etc

  - have various voltage regulators to choose from

- Did not order 0603 resistors

- Maybe use a MOS rather than an NPN transistor

  - Use leaded package for bread-boarding, then surface mount on final design

- Constantly update schematic to account for changes in parts

- Mouser parts should be arriving soon

4.  Board

- Order early

- Will arrive about 1.5 weeks after order

5.  In-depth ZigBee

- Frst step is SPI interface

- From there, move to low-level routines like read/write registers and buffers

- 231 can give status info, 230 is older model

- Need to find how to read/clear the interrupt register and how to mask interrupts

- Riley and Pat will start working on ZigBee

6.  Next Meeting

- Scheduled for 1/20/2009 at 10am

- Angela will be manager, Riley will take minutes