Minutes 1/27/2009

- List of subsystems to be presented at first DR

  - Wireless Communication

    - 1/27 – finished function, from terminal we can read and write data to the register

      - Can we write to state register to make it automatically go to that state? – finite state machine to move from state to state by sending commands to state register on Zigbee transceiver through SPI

      - Make this flow happen  by writing to state register

        - Start off -> move to next state according to diagram

        - Move from next to transceive/receive

        - There is a status register to tell you what state it is in

      - Want to get into state where it is sending and receiving

        - Receive state: turn on a mote, see if getting data showing up

        - Transmit state: packet sniffer

      - SPI transmission tells you how many bytes are in message if you need to know

    - Non-beta version of programmer in LC does not work with the LCD

      - File associated with each part might be wrong in old programmer

      - Natalie loaded on some?

      - Load programmer on personal computers

  - PIR - Can tell if someone is moving -> bit goes high

    - Has about a 20 ft range

    - Seems to know if someone is there or not

      - Just assume if someone is there in 5 minutes

        - Timer going slowly

        - WDT?

        - Have an interrupt to reset timer

        - If timer reaches 0 that means no one

      - Could have a real time clock chip on there

        - When someone moves -> write to the actual time

        - For first DR -> need to have an approach that will work on THIS chip -> Determine how to know IN room

          - Figure out how your system will behave

          - Don’t want to decide you need a certain piece after

  - Batteries

    - Our old mAhr approximations were high, assumed series when it’s parallel

    - Did find 250mA batteries for $10 – 9V Nickel Metal Hydride

      - Our calculations said 600mA would only last 3 days

      - LEDs will use less power – need to make sure we have enough power when they DO come on (last for 20 min)

      - Zigbee just sitting, listening 13.2 mA

      - Might have to use AA for 2500 mA

        - Deal with charging issues

        - Last 2 weeks

      - Can we have the base pods attached to power?

      - Can we coordinate the timing using a real time clock?

        - Only come on for 5 sec to T/R rather than being on the whole min

        - Without this, sync might be an issue

        - Katie – look into real time clock, might be a spot for it on our original board

      - Should we push power off to later?

        - If we have a regulator on board, then we can always change

        - Encouraged to look at bigger picture during design phase

          - Incorporating battery charger needs to be done when making a board

  - Superbright LEDs

    - Really good visibility angle

    - 800 mA  with 3 in series – seems high, check again

    - Each took 1.8 V drop

    - Used a variable supply for 7V, only puts out 500 mA

- Additional questions

  - Should we be looking into plastic container?

    - Polycase has all sorts of different cases

    - Hammond – Digikey has a few

    - At some point adjust board size to case

    - Need to have circuit board against top -> bottom mount LEDs

      - Might be easier to mount all the parts that need to stick out and then connect by wiring harness to the main

      - Might use an outline and use that for placement

  - Heard anything from Microchip?

    - They are not getting back to Dave

    - They have our information, maybe on the way?

  - Are we behind anywhere?

    - Don’t have a whole lot of time for functioning transmission system

    - Keep Dr. Gupta in loop – useful once we get TX/RX

- Action Items

  - Riley and Pat – work towards transmission and reception, talk to Dr. Gupta

  - Angela – re-measure LEDs and try to get our circuit working with the board

  - Dave – talk to Microchip, figure out batteries, look into packaging

  - Katie – determine PIR software, look into real time clock