Team GreenHouse
Minutes Tuesday, February 3, 2009

- List of subsystems to be presented at first Design Review

  - Wireless Communication

    - We can receive packets, sending is in progress and on schedule

      - We need to look into the structure/size of our own packets

    - Continue to keep an eye on the power details of different states in the FSM, especially with the possibly use of the clock

    - Riley/Pat will set up a meeting with Dr. Gupta to go over protocols and synchronization

  - PIR sensor

    - Katie is working on an interrupt service routing that is getting stuck somewhere

      - possible issues with timer or clearing interrupt flag

    - There were troubles when trying to use 3.3V logic on the 1640

      - recheck I/O port settings – these default to analog

    - Determine accuracy, thresholds, calibration

  - Batteries

    - Dave will draft schematic of on-board charging circuit with a charger chip

    - Board file will be updated to include this, plus batter holders upon completion

      - Keystone has picture of holders with dimensions – make Eagle part

  - LEDs (Angela)

    - Current Draws – 1.5mA per LED, all must be in parallel – 10.5mA total

    - Making them flash will draw attention and conserve power, Angela will work on this

  - Real Time Clock

    - Katie found an SPI clock from Dallas Semi that has a backup battery

      - Sample possibly from Maxim

    - WDT may be useful in place of real time clock in sensor applications. For Zigbee considerations, this is pending the talk with Dr. Gupta

- Additional items

  - Microchip Parts arrived TODAY

  - Packaging details

    - Polycase has some good options, but we need a set size

    - We need the LEDs and PIR on the faceplate, and a hole for Zigbee antenna

    - Dave will change schematic with an IDC connector and a ribbon cable for these connections

    - Angela will look into LED holders

  - Temperature sensor

    - This can possibly on board

    - We can use rapid changes in temperature in addition to absolute temperatures to determine the presence of a fire

- Action Items

  - Riley and Pat will continue to work toward transmitting a packet, and talk to Dr. Gupta further about communications protocols and synchronization

  - Katie will continue working to get PIR to work with interrupts on 1640 board and contact Maxim about a Real Time Clock sample

  - Angela will check on LED holders and write code for flashing LEDs

  - Dave will change the schematic for stuff that will be off board and have a preliminary charging circuit design

Next Meeting: 10:00AM Tuesday, February 10, 2009

    - Manager: Dave Venker

    - Minutes: Patrick Cash