Team GreenHouse
Minutes for Tuesday, February 10, 2009

- Subsystems Review

  - Wireless Communication (Pat & Riley)

    - Report on meeting with Dr. Gupta

      - Next step is to make a board receive a command from another board and act on it (e.g., turn on LED)

      - Also need to look at addressing

      - Schafer has another J11 board we can use

    - Discussion of possibility of using RTC for wireless comm.

      - Power consumption considerations are less important than getting network working

      - Better to design the board to be able to use an RTC now, so we can add it in the future if needed

    - Packet data payload

      - Shouldn’t worry about being efficient with packet structure

    - Discussion of alternate code repository - options

      - Webfile public space

      - Google Docs

    - Need to separate libraries for different devices

  - Temp Sensor

    - The 5-pin TC77 part we have now has only 1 data line for SPI

    - Communicating with it would be difficult

      - Would conflict with settings used to communicate with other devices

    - We should look for the 6-pin version of the part

    - Possibility of getting a sample with a demo board from Microchip?

      - Dave will talk to his contact about this

  - PIR Sensor

    - Problem setting up timer to time for 5 minutes

    - Use a counter to effectively multiple the timer length

    - Decrease counter each time timer reaches 0, once counter reaches 0 do X

  - Batteries

    - Charging samples coming in (DIP packages)

    - Schematic updated

      - Charger/wiring harnesses

      - Dave made the library part for the battery holder

    - Routing not updated yet, waiting for further changes

    - Get some batteries

      - Rechargeable NiMH AA’s

      - Schafer has some 3000 mAh’s for us to use

  - LEDs

    - Possibility to Eliminate MOSFETs?

      - 25 mA sources on a pin

      - 200 mA per port

      - Each LED draws 1.5 mA

      - Schafer: use a MOSFET just in case we want to get them brighter later

  - RTC

    - 3 wire vs. 2 wire SPI?

      - Might need to look for new one

    - Need crystal 32.768 kHz

      - Schafer has one for us to use

- Other Items

  - Look at timeline and Action Items

    - Feb 24th is 1st design review

  - Packaging details

    - Needs to be smaller

    - Use standoffs

    - Should try to keep it to 3”x4”

  - Board ordering

    - Depends on when we need more b/c we can’t do something with what we have

    - Parts need finalizing

    - Hopefully order before spring break so we can have them after

    - Order a bunch at a time

    - Send through DFM, Schafer before ordering

    - Done sometime next week