Team GreenHouse
Minutes for Tuesday, March 17, 2009

- Subsystems Review

  - Temp Sensor (Katie)

    - Did we get a board to test the sensor

      - Dr. Schafer has something that may solve this in his office

      - Need a bandsaw or something

  - Batteries (Dave)

    - Demonstrated fast and slow charge

    - Issue with batteries discharging unevenly

      - Stop by and use Schafer’s charger

      - Probably just a “more tired” battery

    - Supplies:  Check on .4 ohm resistor… need something that doesn’t need to order 1000

  - LED’s (Angela)

    - They are working

      - Fixed the resistors – get rid of resistor between MOSFET and ground

  - High level Zigbee programming (Pat and Riley) – Starting this week

    - Store the short address and PAN address and in the nonvolatile EEPROM

    - Adjust geographic locations from the central node only using X-Y coordinate system.

    - Must also include the direction the node is facing!

    - Dr. Schafer: think about packaging and antennas

      - Chip antennas – can couple to that on the board

      - How does 2.4 GHz go through plastic?

      - Get one with chip antenna on it from Dr. Schafer

- Design Review II Time line Review

  - Board routed and submitted

    - Dr. Schafer won’t wait for the other boards – it should go out soon

    - Go through mechanical layout – print out board to scale

  - Demonstration of temp sensor’s fire detection

    - 2 weeks

  - High level coordination between nodes and central

    - 2 weeks

  - Coordinate information flow through system

  - Date? – Maybe first week of April

    - Actual demo is April 30

- Board Update

  - Errors due to net class definitions

    - All the clearance errors taken care of

    - Left with width errors – mostly because of power and GND

      - Make sure we have good power distribution system

      - 30mils is more for stuff spreading around the board

      - Not as important for traces going to each part

      - Look at “prettiness” – as long as you have traces come out the end the small parts will self-align

      - For fine pitch parts you want to make it as wide as can be and that’s good enough

        - Make wider if away from the part for PWR and GND

      - Don’t bother going to a wider trace for a signal once you get out of the fine pitch

      - Should we make DIFFERENT signal classes?

        - Probably can just make the width smaller for all

      - Just don’t miss EASILY fixed clearance errors

        - Can redefine net classes if the whole board is giving you errors

  - How’s our timing looking?

    - Try to get to Schafer tomorrow – run through DFM before

- Next Meeting: 10:00 AM on Tuesday, March 24

  - Manager: Katie Pierret

  - Minutes: Dave Venker