Team GreenHouse
Minutes for Tuesday, March 31, 2009

  - Temp Sensor (Katie)

    - Temp conversion and finding a threshold

      - Katie attempted to fix the old one using the solder sucker

      - Discussion of programming and operation

        - Temp stored as 10-bit two’s compliment int

        - Should stored internally in our program in 100th of degrees, as to avoid using float variables

        - Should be able to find a good threshold value

  - High level Zigbee programming

    - Packet header problem fixed and sniffer reads source address correctly

    - Multiple nodes running – occasional failed sends

      - Disable interrupts during read int status register

      - Should set it up to deal with failed sends

    - Store the short address and PAN address and in the nonvolatile EEPROM (Dave)

      - Disable interrupts during write

      - Write via programmer/program

    - Other considerations

      - Need to make nonvolatile bits for easy porting (Riley)

      - Test zigbee distance

  - GUI (Katie/Angela/Dave)

    - Discuss meeting with Steve

    - Need to define requirements

      - Simulate fires

      - Buttons

      - Different layouts

  - Coordinate exit pathways (?) – work on this in GUI?

    - Should we coordinate exit way on PC?

  - Board Update

    - ORDERED! Should arrive by the end of next week.

  - Parts Update – review spreadsheet

    - LEDs, charger ICs, RTC, SPI EEPROM, PIR, VReg, others?

      - LEDs and PIR not ordered yet

Next Meeting: 10:00 AM on Tuesday, April 7

Manager: Pat Cash

Minutes: Angela Comana