Eroding Sines--Minutes 2/24/2010

- Kat

  - Siteplayer not working in LC –different VLAN

  - Works upstairs

    - Working on resolution

- Scott

  - Working on Site player ( microcontroller

  - LLD for siteplayer written

  - Started LLD for Zigbee

- Mike

  - Parts

  - Siteplayer draws ~60 mA

- Dane

  - Measured relay current

    - 30mA @ 3.5v

    - Can run straight from power brick at 9v

  - Put diode on relay to prevent backwards current spike

  - Resistor on MOSFET to pull-down

  - Need to find smaller MOSFETs

Demo will be held in the LC

Final presentation will be held in the LC—all EE faculty will be invited

To do:

Look into using a different microcontroller with .8mm spacing