## Slide 1: Athletic Trainer Pads
Team Graduate: Kate Hjorth, Adrienne Miller, Addison Azar, Mike Guyette, Caroline Cho

## Slide 2: Introduction

## Slide 3: Problem Description
Speed and agility drills which rely on user timing and user setup have human error
No standard for how to analyze data of reflex, accuracy, and endurance of these drills of over a period of time
Training drills are not automatically catered for the individuals without knowing strengths and weaknesses

## Slide 4: Proposed Solution
Create a system that interfaces between a standardized physical activity measuring reflexes and an app that can analyze the data and grow with the user
Hardware
  Four distinct circuits containing a pushbutton and LED encased in an enclosure
  Pads will be structured to trigger the spring-loaded button once touched
  Pads should be oriented in a square around the user, who will begin the drill in the middle
Software
  Pads interface to app via ESPNow (short message protocol that works with ESP32)
  User can choose how many runs to perform, the difficulty, and the type of test being run
  Collect and stores the user’s data for longtime analysis
  Produces user-friendly graphs to track progress over any time frame
  Performs simple machine learning to update drills based off user’s unique needs

## Slide 5: Demonstrated Features
4 Pads with addressable LEDs that light up
Ability of pads to detect touch
App interface that connects to pads through ESP Now
Drill options to test reflex, accuracy, endurance
Real-time data collection of time between light up and touch & accuracy of touch
Data storage of accuracy/time with analysis of trends over time
Machine learning to change drills based upon user trends

## Slide 6: Available Technologies
Gebildet Stainless Steel Waterproof Push Button
STARELO Stainless Steel Waterproof Push Button
NeoPixel Jewel - 7 x 5050 RGBW LED
ESP32-WROOM

## Slide 7: Engineering Content
4 Identical Sensor Circuits
  Receive power from batteries
  Cue and Feedback System
  Interface with ESPNow
Physical Sensor Pad Structure
  Visible addressable LEDs
  Spring-loaded button
  Durable and weather resistant
App Interface
  Connect with ESPNow
  Pre-session user inputs & transmission of parameters and LED
  Receive feedback from sensors
  Store and assess data according to evaluation metrics
  Generate and display an evaluation report
  Machine learning

## Slide 8: Conclusion
What: Athletic Trainer Pads with connectivity to app interface in order to detect, store, and improve user ability in speed and reflexes
Why: Allowing users to move beyond traditional methods of measuring speed / improving agility will improve efficiency for athletic testing and physical therapy

## Slide 9: Questions?